## Slide 1
09 December,2021
PRESENTATION ON
Different Types Of Communication used in Smart Metering System with advantage & disadvantage
Mahmud Munim
Network Engineer,ICT,BREB

## Slide 2
Overview of Prepaid Smart Metering System.
Different communications media overview and comparison among them based on Rural Electrification scenario.
Communication media proposal for Rural Electrification System.
Recommendation to select comunication media for Rural
Electrification System.
Advantage of Prepaid Smart Metering in Rural Electrification System.
Content

## Slide 3
PLC
Office
Overview of Smart Metering System

## Slide 4
HES
Load Control.
Schedule Meter Reading .
Communication Analysis.
Group Programming.
Event Collection.
Demand Side Management.
DCU
Data concentrators collect data about energy consumption and other customer management information from smart meters connected via a wireless or power-line communication (PLC)
Communication
GPRS: 3G
Easy troubleshooting
expensive
PLC: G3-PLC
Good grid environment
low noise disturbing and signal attenuating
High maintenance cost
RF: RF mesh
Broadcast Remotely
RF mesh to make less DCU
MDM
Loss Management
Anti-tampering
Monitoring analysis
Custom report
Module
Meter
HES
MDM
Billing
Working Procedure of Smart Metering System

## Slide 5: Communications scenario on Rural Electrification System.
MDM
DLMS G
DLMS G
DL
PLC
HES

## Slide 6
Real Scenario in PBS: 1 Proposal 1: PLC/RS-485
Inside in building where RF or GPRS will not work properly.
In this scenario G3-PLC or RS-485 is suitable for data exchange.
G3-PLC ( Communication media)
Smart meter
HES (server located in BREB)
DCU

## Slide 7
Real Scenario in PBS: 2 Proposal 2: RF-Mesh
RF-Mesh (Communication media)
Large number of consumer within 1 or 1.5 km area where high raise building is not available.
In this case RF-Mesh is suitable for data exchange.
PLC / GPRS is costly in this case because need more SIM card/DCU to implement communication structure.
HES (server located in BREB)
Smart meter

## Slide 8
Real Scenario in PBS: 3 Proposal 3: GPRS
Small number of consumer in 1 or 1.5 km area.
In this case GPRS is suitable for data exchange.
PLC / RF is costly in this case because need more DCU to implement communication structure.
GPRS (Communication media)
Smart meter
HES (server located in BREB)

## Slide 9: Thanks